## Slide 1: Media Cognition Project Report
Song Chuan Lim, Ziyi Chen, Yudong Xie, Hao Chen
Electronic Engineering Department, Tsinghua University
2024年12月23日

## Slide 2: Table of contents
Apriltag & Proposal & Match
Robotic Arm
Audio & Human Interaction
Demo Video

## Slide 3: Module Apriltag
Main Function
  Detect two-corner AprilTags using template matching.
Input
  A single image captured by camera.
Process
  Use cv2.matchTemplate to directly match the AprilTag template in the image.
  Tricky, but robust!
  Compute coordinates.
Output
  Center coordinates of AprilTags.
Notes: Coordinate System

## Slide 4: Module Proposal
Main Function
  Detect objects in given image using YOLO, robust for orientation by 90°, 180° or 270°
Input
  A PIL Image.
Process
  Detect objects in the original image using YOLO.
  Rotate the image by 90°, 180°, 270° and detect objects at each angle.
  Coordinate transformation and deduplication.
Output
  Object labels and coordinates in initial coordinate system.
Notes: Coordinate System

## Slide 5: Module Match
Main Function
  Identify the best matching image for a given text or the best matching text for a given image using CLIP.
Input
  A piece of text with multiple images, or an image with multiple text descriptions.
Process
  Encode the input text and images into a shared embedding space using CLIP.
  Compute similarity scores between the texts and images using CLIP.
  Identify the highest similarity score and its corresponding index.
Output
  Index of the most relevant image/text and the similarity score.
Text: Put clock in red bin
Image:
0. 1.
2. 3.
Output:
Max probability: 0.9985 Max index: 2
Notes: Coordinate System

## Slide 6: Robotic Arm - Fundamentals
Move
  send_coords()
  Release the servos, use the function get_coords() to get the coordinates, and record them as fixed parameters.
  Cooperate with time.sleep() to realize initialization and path planning.
  Core: The coordinate system of the robotic arm and that of the camera and YOLO are different, so the key is to solve the coordinate transformation.
Get & Put
  set_basic_output()
  The port number of the pump is 2 & 5 (fixed)
  Set the parameter to 0 means to open the air pump, and set to 1 means to close the air pump.
  Picking up process: Move above the object (via transfer point) --> Descend while turning on the air pump --> (Suck it up) Rise to a certain height
  Placing down process: Hold the object above the corresponding bucket (fixed position) --> Turn off the air pump --> Restore

## Slide 7: Robotic Arm - Coordinate Transformation
Crop
  Image.crop()
  Extracting specified pixel points from the camera image
  Since it is rough cutting, appropriately wider is okay.
  This part is also fixed parameters.
Apriltag
  set_basic_output()
  Comparison on the cropped image
  Return value: Horizontal and vertical coordinates of the upper left and lower right AprilTags (april_ul_x, april_ul_y, april_br_x, april_br_y)
  At the same time, record the coordinates of the two AprilTags with the robotic arm, thus establishing the mapping relationship from the robotic arm coordinate system to the image coordinate system.
x
y

## Slide 8: Robotic Arm - Coordinate Transformation
YOLO Location
  Yolo will return the detected object’s top-left and bottom-right pixel coordinates (ul_x, ul_y, br_x, br_y), which are in the same coordinate system as apriltag.
  Use relative coordinates (normalized) to control the robotic arm uniformly.
  Relative coordinates (formed by two tags) are calculated as follows:

## Slide 9: Robotic Arm - Coordinate Transformation
Robotic Arm Location
  The calibration is performed based on the coordinates of two pre-determined AprilTags. It is known that the coordinates of the two tags in the robotic arm coordinate system are (B_TOP, B_LEFT) and (B_BOTTOM, B_RIGHT).
  The default top-left corner is (0, 0), and the bottom-right corner is (1, 1).
  The coordinates of the robotic arm (the first two axes in the six-axis coordinate system) are calculated as follows:
  Attention: The relative coordinates here are opposite to the xy coordinates of the robotic arm!

## Slide 10: Audio —— Human Interaction
openai-whisper：Robust speech-to-text
  is_silent(audio_data)：Silence detection
  transcribe_audio(audio_data)
  listen_and_recognize()

## Slide 11: Audio —— Human Interaction
zhipuai：Robust Understanding

## Slide 12: Audio —— Human Interaction
Example

## Slide 13: Contribution
Audio: Song Chuan Lim
Proposal & Apriltag: Ziyi Chen
Match: Ziyi Chen, Song Chuan Lim
Robotic Arm: Yudong Xie, Ziyi Chen
Integration Test: Yudong Xie, Song Chuan Lim, Ziyi Chen

## Slide 14: THE END & ENJOY THE DEMO
Song Chuan Lim, Ziyi Chen, Yudong Xie, Hao Chen
2024年12月23日

## Slide 15: Demo